## Slide 1: Computer Systems Architecture

## Slide 2: Memory

## Slide 3: Motivation
In real life memory is finite
Fast memory is expensive
Memory access is critical to overall performance
Lots of research on processor-cache interface
Main and virtual memory organization is yet another performance bottleneck

## Slide 4: Memory Hierarchy
Cache Static RAM
5-25 ns access time
Cost/MByte highest
Main Memory Dynamic RAM
60-120 ns access time
Cost/MByte high
Hard Disk
10-20 million ns
Cost/MByte low

## Slide 5: Memory Hierarchy

## Slide 6: Goals of Hierarchical Memory Design
Achieve an average memory access time that is almost as fast as the fastest memory level
Achieve an average price per bit that is as low as the lowest memory level
Use lessons learned from locality principle for both data and instructions
Achieve overall high and cost-effective performance

## Slide 7: Memory Strategies
Make entire memory fast
Separate concerns: segregate instruction memory from data memory if dual-port memory is available
Make memory ports wide so that can access larger chunks
De-randomize memory access by clever programming or compilation
Encourage prefetching to the largest extent possible
Create a memory hierarchy to keep hot items in fast memory
Use principle of locality

## Slide 8: Key Idea
Make the common case fast
Common  Principle of locality
Fast  Smaller is faster

## Slide 9: Principle of Locality
Temporal locality
  Locality in time
  If a datum has been recently referenced, it is likely to be referenced again
Spatial locality
  Locality in space
  When a datum is referenced, neighboring data are likely to be referenced soon

## Slide 10: Basic Terminology
Cache -- name given to the first level of memory seen from the CPU
Miss rate -- fraction of memory accesses that are not in the cache
Miss penalty -- additional clock cycles needed to service a cache miss
Hit time -- time to hit in the cache
Block -- smallest unit of data that can be accessed from main memory

## Slide 11: Cache Performance Review
CPU execution time = (CPU clock cycles + Memory Stall cycles) x Clock cycle time
Memory stall cycles = Number of misses x Miss penalty

## Slide 12: Example
CPI=1 when all memory accesses hit in cache
Loads and stores are 50% of the instructions
Miss penalty is 25 clock cycles
Miss rate is 2 %

## Slide 13: The Cache
5600
1000
0
1016
2447
1048
43
1028
4 Most recently accessed Memory locations (exploits temporal locality)
Issues:
How do we know what’s in the cache?
What if the cache is full?
Cache
5600
1000
3223
1004
23
1008
1122
1012
0
1016
32324
1020
845
1024
43
1028
976
1032
77554
1036
433
1040
7785
1044
2447
1048
775
1052
433
1056
Main Memory Fragment

## Slide 14: Basic Cache Questions
Block placement
  Where can a block be placed in the cache?
Block Identification
  How is a block found in the cache?
Block replacement
  Which block should be replaced on a miss?
Write strategy
  What happens on a write?

## Slide 15: Q1: Block Placement
Fully associative
  arbitrary location in cache
Direct mapped
  each block has a unique location in the cache
  Block_index = Block_address mod Number_of_blocks
Set associative
  arbitrary location within unique set
  Set_index = Block_address mod Number_of_sets
  Number_of_sets = Number_of_blocks/ Number_of_blocks_per_set

## Slide 16: Direct Mapping
Index
Tag
Always zero (words)
Valid
Tag
Data
Index
Cache
5600
3223
23
1122
0
32324
845
43
976
77554
433
7785
2447
775
433
3649
Main Memory
00 00 00
00 01 00
00 10 00
00 11 00
01 00 00
01 01 00
01 10 00
01 11 00
10 00 00
10 01 00
10 10 00
10 11 00
11 00 00
11 01 00
11 10 00
11 11 00
6-bit Address
5600
00
Y
775
11
Y
845
01
Y
33234
00
N
In a direct-mapped cache:
-Each memory address corresponds to one location in the cache
-There are many different
memory locations for each cache entry (four in this case)
00
01
10
11

## Slide 17: Hits and Misses
The hit rate and miss rate are the fraction of memory accesses that are hits and misses
  Typically, hit rates are around 95%
Many times instructions and data are considered separately when calculating hit/miss rates
When the CPU reads from memory:
  Calculate the index and tag
  Is the data in the cache? Yes – a hit, you’re done!
  Data not in cache? This is a miss.
    Read the word from memory, give it to the CPU.
    Update the cache so we won’t miss again. Write the data and tag for this memory location to the cache. (Exploits temporal locality)