## Slide 1: Computer Systems Architecture

## Slide 2: Cache Mapping
Problems

## Slide 3: Problem 1
Consider a direct-mapped Cache with 64 blocks and a block size of 16 bytes. To what block number does byte address 1200 map?

## Slide 4: Problem 1-- Solution
Step-1:
You have to find the block size first.
1 block = 16 bytes
Step-2:
Then find the memory block number that byte address 1200 belongs to.
Since 1 block is 16 bytes,
byte address 0 ~ 15 : block 0
16 ~ 31: block 1
32~ 47: block 2
…
Therefore,
floor (byte address / block size) = memory block #

## Slide 5: Problem 1-- Solution
So floor( 1200/16) = 75.
Step 3:
Then you need to find which cache block memory block 75 maps to.
In a direct-mapped cache,
cache block # = memory block # mod (total block number of cache)
Therefore, 75 mod 64 = 11.

## Slide 6: Problem 2
Consider a 2-way set associative cache with 64 blocks and a block size of 16 bytes. To which set number does byte address 1200 map?

## Slide 7: Problem 2-- Solution
Step 1:
Since the cache is 2-way set associative, a set has 2 cache blocks. Because there are 64 cache blocks, there are 32 sets in the cache (set 0 ~ set 31).
Step 2:
Byte address 1200 belongs to memory block 75.
Then
set # = memory block # mod (total sets in the cache).
Therefore, 75 mod 32 = 11.
So memory block 75 maps to set 11 in the cache (cache block 22 and 23) and chooses one of them. How to choose one of them is a very long story.

## Slide 8: Problem 3
A 64KB cache has 16 byte blocks. If addresses are 32 bits, how many bits are used the tag, index, and offset in this cache?

## Slide 9: Problem 3-- SOLUTION
For Direct Mapped Cache
Number of bits for addressing word= 4bit
Number of cache lines = Size of cache / size of Block
64KB/16B = 4K = 12bits
Remaining 16 bits for tag so division of 32 bits is like
TAG | GROUP | OFFSET
16 bits | 12 bits | 4 bits

## Slide 10: Problem 3-- SOLUTION
For 4-way set associative Cache
Number of bits for addressing word= 4bit
Number of lines/blocks in each cache set is 4
so each cache set is 4*16B = 64B
Number of cache sets = size of cache/size of cache set
64KB/64B = 1K
TAG | INDEX | OFFSET
18 bits | 10 bits | 4 bits

## Slide 11: Problem 3-- SOLUTION
For Fully Associative Cache
Number of index bits = 0 because any block can be stored in any line

## Slide 12: Problem 4
What will be the final cache contents for a Fully associative cache with one word blocks and a total size of 6 blocks?
Use LRU replacement. For each reference identify the index bits, the tag bits, the block offset bits, and if it is a hit or a miss
Caches are important to providing a high-performance memory hierarchy to processors. Below is a list of 32-bit memory address reference, given as word addresses 21, 166, 201, 143, 61, 166, 62, 133, 111,143, 144, 61

## Slide 13: Problem 4-- SOLUTION
Cache index | Address in Cache | Hit/ Miss
0 | 21,62 | MM
1 | 166,133 | MM
2 | 201,111 | MM
3 | 143 | MH
4 | 61,144 | MM
5 | 166,61 | MM
Caches are important to providing a high-performance memory hierarchy to processors. Below is a list of 32-bit memory address reference, given as word addresses 21, 166, 201, 143, 61, 166, 62, 133, 111,143, 144, 61

## Slide 14: Problem 5
What will be the final cache contents for a Direct Mapped cache with two word blocks and a total size of 24 blocks?
Use LRU replacement. For each reference identify the index bits, the tag bits, the block offset bits, and if it is a hit or a miss
Caches are important to providing a high-performance memory hierarchy to processors. Below is a list of 32-bit memory address reference, given as word addresses 21, 166, 201, 143, 61, 166, 62, 133, 111,143, 144, 61

## Slide 15: Problem 5--SOLUTION
What will be the final cache contents for a Direct Mapped cache with two word blocks and a total size of 24 blocks?
21, 166, 201, 143, 61, 166, 62, 133, 111,143, 144, 61